## Slide 1
PARTICLE DETECTION
How the system works
A classical image-processing pipeline that ignores the repeating circuit pattern on a wafer and keeps compact contaminant particles.
20–100 µm
Size that is reported
Per tile
Never on the full mosaic
DoG first
ML only scores those hits
Outputs: particles.csv · mosaic_overlay.jpg · optional N/S/E/W combine

## Slide 2
END TO END
From a folder of tiles to a particle table
Detection runs one image at a time. The stitched JPEG is a report, not an input.
Find tiles
Match R{run}_{row}_{col}_{mag}X. Unmatched files still load.
1
Place on a grid
Origin is the smallest row and column. Step size uses the overlap fraction.
2
Load in parallel
Each thread: RGB → gray float32, then drop the full image.
3
Preprocess
Denoise, divide out slow illumination, stretch contrast to 0–1.
4
Remove the pattern
FFT notch when the lattice is periodic. Otherwise a white top-hat.
5
Find compact blobs
Difference of Gaussians, then size, border, and shape gates.
6
Score and merge
Optional ML. Map to global nm. Merge overlap and N/S/E/W duplicates.
7
Write the report
particles.csv and a downsampled mosaic with a red circle on each hit.
8
continues
Particle detection on structured wafers
2 / 10

## Slide 3
TILES
Discovery, placement, and preprocessing
Each worker handles one image. Neighbouring tiles are merged only after detection.
Why not the mosaic?
Tiles are multi-megapixel. A full-resolution stitch would need tens of gigabytes.
Each tile can have its own pitch. A notch built on the first tile is wrong for the rest.
Overlap would be processed twice, and illumination would mix.
The JPEG is assembled later from small thumbnails. It is a report.
Image folder
TIFF, BMP, PNG, or JPEG
Match the filename
R{run}_{row}_{col}_{mag}X
Optional run and mag filters
Place on the filename grid
Origin = minimum row and column
x0, y0 from overlap step
Load → gray float32
Integer images divided by their max
Colour is discarded
Denoise, flatten, stretch
Blur 1 px · illumination σ 160 px
1st–99th percentile → [0, 1]
Preprocessed tile
Ready for pattern removal
No filename match
Still detected.
Skipped on the mosaic.
Typical: N, S, particles_only
Parallel workers
0 uses every core.
OpenCV stays on one thread so the pool does not oversubscribe.
Particle detection on structured wafers
3 / 10

## Slide 4
BACKGROUND
Remove the lattice, keep the flake
A particle is a compact irregular bright flake. Pads, letters, and lattice nodes are the false positives.
Preprocessed tile
Lattice peaks
in this tile’s FFT?
Yes — notch those peaks
Zero bins ≥ 0.35, dilated by 3. Keep DC.
Per-tile mask. A large tile checks a thumbnail first.
No — white top-hat
Opening radius 50 px, which must exceed the flake.
Also used when method is tophat, or the notch is empty.
Yes
No
If particles are dark, invert the residual so later steps still look for bright blobs
Local SNR
Boost isolated blobs, suppress long edges. Skipped on a top-hat residual.
Protect islands
Compact components ≥ 20 µm. Flakes ≥ 40 µm stay even on a corner.
Soft borders
Wide ramp around region edges. Islands keep at least 0.85 of the ramp.
Particle detection on structured wafers
4 / 10

## Slide 5
DETECTION
Blobs, gates, and the optional model
Difference of Gaussians proposes hits. Every later step only accepts or rejects those hits.
Scale to 0–1 and zero anything below prominence 0.30
Search σ 3.7 → 36 (~10–100 µm at 0.96 µm/px). Keep measured size 20–100 µm.
DoG peaks
Geometric scales, ratio 1.4, threshold 0.12. Island centroids are seeded in. Overlap keeps the larger scale.
Measure the photo
Equivalent circular diameter from pixels that stand out on the preprocessed image, not the residual.
Intensity
Residual at the peak ≥ 0.30 prominence and ≥ 0.50 confidence.
Border and shape
Drop hits within 12 px of a region border unless the island is protected. Require a local peak and compact support.
Structure
Drop clusters (≥ 2 neighbours within 48 px) and long axis-aligned rows, unless the hit is clearly larger.
Optional ML
v5 is ExtraTrees on an unmarked crop. No CNN. Default order: gates, then structure, then this score.
Dropped along the way
Lattice nodes and grain below the prominence floor
Pad corners, box rims, and the tile frame
Specks under 20 µm and flakes over 100 µm
Beads in a row just inside a layout box
Hits the model calls layout, when ML is on
Circularity stays off. Real flakes are often less round than letters.
Particle detection on structured wafers
5 / 10

## Slide 6
AFTER EVERY TILE
Global coordinates, de-duplication, and files
The same physical speck on two overlapping tiles becomes one row.
Grid tiles
N / S / E / W and particles_only
Local pixels → mosaic pixels
Add the tile origin from the filename grid.
Merged on their own
Stems N, S, E, W, and particles_only are not mixed into the 8 px grid merge.
Mosaic pixels → nanometres
Multiply by pixel_size_nm. At 5× that is 960 nm (0.96 µm).
Wider match
Search radius is at least 24 px, or 0.4 × the larger diameter.
Sort by confidence
Residual intensity at the peak, highest first.
One hit per direction
Two detections on the same N image never merge with each other.
KD-tree merge
Neighbours within 8 px (~7.7 µm) collapse to the best hit. Size is the max.
Record the views
nsew_count and nsew_dirs list which lighting angles agreed.
Both streams are numbered 1…N and written to the same two files
particles.csv
id, global nm, size, confidence, source tile, N/S/E/W fields
mosaic_overlay.jpg
~20 MB thumbnail stitch. Red circle per hit. Unplaced files omitted.
Particle detection on structured wafers
6 / 10

## Slide 7
SECOND ENTRANCE
N / S / E / W directional lighting
This combine step does not run blob detection. It builds images the main pipeline can detect on.
N
North
S
South
E
East
W
West
Flatten each angle with a Gaussian, σ 120 px
Keep pixels that are bright in at least 2, 3, or 4 of the 4 angles
Repeated for k = 2, 3, and 4
Combi
Isotropic brightness
Particles only
Otsu mask, compact shapes
Symmetry
How many angles agree
Then the main detector, with NSEW settings
3.5 µm/px · denoise σ 0.5 · blob σ from 9 · blob threshold 0.3 · ML threshold 0.55
Directional hits merge afterward: at most one per lighting angle.
Particle detection on structured wafers
7 / 10

## Slide 8
MACHINE LEARNING
The model only scores blobs DoG already found
It answers particle versus not-particle. It does not search the wafer, and it does not name a particle type.
DoG proposals
The only source of candidates. Debris the blob detector missed is never scored.
Cheap gates
Size, confidence, border distance, local peak, and compact support.
Structure filters
Drop clusters and axis-aligned rows. This runs before ML unless you flip the order.
P(particle)
v5: ExtraTrees on an unmarked crop of the photo and the residual. No CNN.
Keep or drop
Keep the hit only when the probability is at least ml.threshold.
Limits
Not a neural detector. Pitch, magnification, and lighting still mean retuning the classical steps.
Labels sit on detector hits, so a miss cannot be recovered here.
ml.enabled with a missing joblib raises. It will not quietly run classical-only.
score_before_structure is false. Scoring first can let lattice neighbours cluster-kill a real flake.
Particle detection on structured wafers
8 / 10

## Slide 9
AT INFERENCE
v5 scores each crop with ExtraTrees
The shipped file is a patch model. It has no CNN, so nothing is sent to a second network.
96×96 patch, two channels
Corrected photo and the detection residual, centred on the hit. Circled label JPEGs are never read.
HOG, texture, and layout
Gradient histogram and local binary pattern on both channels, plus shape and the residual features already measured.
ExtraTrees
Class-weighted trees. An isotonic calibrator turns the vote into P(particle).
Keep or drop
Standard threshold is 0.0165, a keep-all setting on the R4 holdout. NSEW uses 0.55.
v5 file
particle_clf_v5.joblib
Kind is patch. The CNN slot is empty, so scoring stops after the trees.
315 labeled hits in the fit: 39 particle, 276 not-particle.
The 0.20–0.80 band in config is only for a cascade file. v5 does not read it.
Particle detection on structured wafers
9 / 10

## Slide 10
TRAINING
A new version from labels, never from the red circles
v5 was fit as a patch model · folds are grouped by tile · the red circles are not training data
1
Join the tables
labels.csv matched to detection rows. Only particle and not-particle.
2
Cut unmarked patches
Source image plus residual, 96×96. Crops under labels/crops/ are ignored.
3
Fit ExtraTrees
Class-weighted trees on HOG, texture, shape, and the residual features.
4
Calibrate and threshold
Isotonic map, then the keep-all cut near 0.0165 on the holdout.
5
Write the next file
A new particle_clf_vN.joblib. The existing v5 file is left as it is.
Reference model
v5 — patch
ExtraTrees on the crop. This is what Detection loads. No CNN.
v4 — residual
Older model. Only the dozen detection numbers, no image crop.
Not in v5
A CNN-on-the-uncertain-band trainer still exists in the code. The v5 file does not use it.
The usual loop
1 Run Detection, with or without the current model.
2 Tinder tab: label new hits. Keys you already labeled, including N/S/E/W aliases, are skipped.
3 Train the next vN, point ml.model_path at it, and set ml.threshold.
Particle detection on structured wafers
10 / 10